INA122 instrument amplifier board

Wire#	Color	Len:	From:	Function:		To:	Function:

1	Blk	1.5	D2	Term 1			I6	Gnd

2	Yel	1.25	F4	V- to cap1 to gnd	F8	to -5v Reg via wire 14

3	Red	1.75	D4	Term2			F10	+5v reg

4	Blu	1.5	D6	Term 3			G2	Vin-

5	Grn	1.75	D8	Term 4			G3	Vin+

6	Red      1.25    D10	Term 5, High batt + 	F12	Reg + raw input

7	Blk	1.25	D12 	Term 6, High batt -      I12 	Gnd

8	Blk	1.25	D14	Term 7, Low batt +	I13	Gnd

9	Grn	1.25	D16	Term 8, Low Batt -	F15	Reg- Raw input

10	Blk	1.25	D25	Term10, Dataq	I12	Gnd

11	Yel	1.25	H25	1k LED Resistor	F16	Regulated -5v

12	Blk	1.25	I7	Gnd			L4	INA pin 5 “Ref”

13	Red	1.75	G10	Regulated +5v		L2	INA pin 7 “V+”

14	Yel	1.5	G8	INA pin 4 “V-“	G16	Reg -5v

15	Blk	1.0	O2	Cap2 via solder	M4	Gnd via wire 12						bridge to N2

16	Blu	2.25	L3	INA pin 6 “Vo”	D18	Term9, Dataq signal

17	Red	2.25	E10	Term 5 via solder	D22	LED +9v unreg						bridge to D10

18	Grn	2.25	G1	INA Pin 1, gain 1	Q5	Output, 1k cermet pot

19	Grn	1.25	K1	INA Pin 8, gain 1	Q7	Wiper, 1k cermet pot

_____	  _____  _____  _____    __________________  _____    ____________________

_____	  _____  _____  _____    __________________  _____    ____________________

Components:

INA122  Instrument Amplifier

Pin#	Port:	Bridged to:	Function:

__1__  _H1__	__________	__Rg___________________________________________

__2__  _H2__	__________	__Vin-__________________________________________

__3__  _H3__	__________	__Vin+_________________________________________

__4__  _H4__	__________	___V-__________________________________________

__5__  _K4__	__________	__Ref (gnd) _____________________________________

__6__  _K3__	__________	__Vo __________________________________________

__7__  _K2__	__________	__V+__________________________________________

__8__  _K1__	__________	__ Rg __________________________________________

Capacitor 1   - 1mfd

__1__ H8__	__________	________________________________________________

__2__ I8___	__________	________________________________________________

Capacitor 2   - 1mfd

__1__ M2___	__________	________________________________________________

__2__  N2___	__________	________________________________________________

Voltage Regulator 1 – LM78LO5

__1__ H10___	__________	____O____ Output, regulated voltage , +5v____________

__2__ I11__  __________	____G_____ Ground _____________________________

__3__ H12___	__________	____I_____ Input, raw voltage, high battery +9v________

Pin#	Port:	Bridged to:	Function:

Voltage Regulator 2 – LM79LO5

__1__    I14	__________	___G___ Ground ________________________________

__2__   H15	__________	___I____ Input, raw voltage, -9v ___________________

__3__   H16  ________		__O___Output, regulated voltage, -5v ___________

Potentiometer – Cermet 1K 15 turn

__1__  O5__	__________	____Output, 1k cermet pot ______________________

__2__  P7__	__________	____ Wiper, 1k cermet pot _______________________

__3__  O10__	__________	____ Not used, but soldered for stability______________

Resistor – 1k ¼ watt

__1__  _____	__________	___  Reduce voltage to power LED __________________

__2__  _____	__________	___Ground to LED   ____________________________